## Slide 1: Mobile security: SMS and WAP
Job de Haas <job@itsx.com>

## Slide 2: Overview
Mobile security
What are GSM, SMS and WAP?
SMS in detail
Security and SMS?
Security and WAP?
What can we expect?

## Slide 3: What is this talk not about
Not about the underlying wireless technologies GSM, CDMA, TDMA
Not from a GSM/SMS/WAP implementer point of view.
Not about actual exploits and demonstrations of them.

## Slide 4: What is this talk about?
General perspective on security of mobile applications like SMS and WAP.
From an external point of view, based on ~10 yrs experience in breaking systems and applications.
Identifying potential problems now and in the near future.

## Slide 5: Who is this talk for?
People asked to evaluate security of SMS and WAP applications.
People who want to do research into SMS and WAP security.
People familiar with computer and Internet security but not with SMS and WAP.

## Slide 6: Mobile Security
General issues:
  Good User Interface paramount for security but very poor.
  Standards tend to omit security except for encryption (and some authentication).
  Creating yet another general purpose platform with associated risks.

## Slide 7: What are GSM, SMS and WAP
Cell phone technologies: GSM, TDMA, CDMA, …
Short Messaging Service: SMS
  Paging style messages.
Wireless Application Protocol: WAP
  ‘mobile’ Internet. A simplified HTTP/HTML protocol for small devices.

## Slide 8: Standards
GSM specific standards GSM xx.xx
ETSI Special Mobile Group (SMG)
  new numbering scheme.
3GPP (move towards UMTS)
  new numbering scheme
WAP Forum. WAP related standards WAP 1.1 / WAP 1.2
Notes: European Telecommunications Standards Institute (ETSI) http://www.etsi.org
3rd Generation Partner Program http://www.3gpp.org
www.wapforum.org

## Slide 9: SMS
SMS Description
SMS Format
Short Messaging Service Centre (SMSC) Protocols
SMS Features: Smart SMS, OTA, Flash SMS

## Slide 10: What is SMS?
Store and forward messaging (PP and CB)
Delivered through SS7 signaling
140 bytes data (160 7 bit chars)
From anything that interfaces to a SMSC:
  Cell phone, GSM modem,PC dial-in,X.25 …
Specifications at: http://www.etsi.org
Notes: “Technical realization of the Short Message Service (SMS).”
GSM 03.40 (now: ETSI TS 100 901)
See also: GSM 03.38 (ETSI TS 100 900), GSM 03.42 (ETSI TS 101 032)

## Slide 11: SMS network elements
E
E
E
E

## Slide 12: SMS data format
Abbrv:
  SC: Service Centre
  MS: Mobile Station
Basic types:
  SMS-DELIVER (SC  MS)
  SMS-DELIVER-REPORT (SC  MS)
  SMS-SUBMIT (MS  SC)
  SMS-SUBMIT-REPORT (MS  SC)
  SMS-COMMAND (MS  SC)
  SMS-STATUS-REQUEST (MS  SC)
Notes: http://www.dreamfabric.com/sms/

## Slide 13: SMS-SUBMIT
 | Description | Size | Mandatory
TP-MTI | Message Type Indicator | 2 bit | Y
TP-RD | Reject Duplicates | 1 bit | Y
TP-VPF | Validity period format | 2 bit | Y
TP-RP | Reply Path | 1 bit | Y
TP-UDHI | User Data Header Ind. | 1 bit | N
TP-SRR | Status Report Request | 1 bit | N
TP-MR | Message Reference | Int | Y
TP-DA | Destination Address | 2-12 byte | Y
TP-PID | Protocol Identifier | 1 byte | Y
TP-DCS | Data Coding Scheme | 1 byte | Y
TP-VP | Validity period | 1/7 byte | Y
TP-UDL | User Data Length | 2 byte | Y
TP-UD | User Data | ? | N

## Slide 14: SMS-DELIVER
 | Description | Size | Mandatory
TP-MTI | Message Type Indicator | 2 bit | Y
TP-MMS | More Messages to Send | 1 bit | Y
TP-RP | Reply Path | 1 bit | Y
TP-UDHI | User Data Header Ind. | 1 bit | N
TP-SRI | Status Report Ind. | 1 bit | N
TP-OA | Originating Address | 2-12 byte | Y
TP-PID | Protocol Identifier | 1 byte | Y
TP-DCS | Data Coding Scheme | 1 byte | Y
TP-SCTS | SC Time Stamp | 7 byte | Y
TP-UDL | User Data Length | 2 byte | Y
TP-UD | User Data | ? | N

## Slide 15: User Data Header
Septets can be octets for 8-bit SMS messages

## Slide 16: User Data Header Elements
IEI | Meaning
0 | Concatenated 8-bit ref.
1 | SMS message indication
4 | 8-bit port
5 | 16-bit port
6 | SMSC control param
7 | UDH source indicator
8 | Concatenated 16-bit ref.
9 | WCMP
70-7F | SIM Toolkit security
80-9F | SME to SME specific use
C0-DF | SC specific use

## Slide 17: Smart SMS/OTA
Joined Ericsson/Nokia spec
Allow sending of ‘smart’ information:
  Ringtones
  Logo’s
  Vcard/Vcal (business cards)
  Configuration information (WAP)
Based on UDH with app specific port numbers.
Notes: “Smart Messaging Specification”, Nokia, version 2.0.0

## Slide 18: Short Message Service Centre
The SMSC plays a central role in the delivery and routing of the SMS.
Every vendor has his own protocol to talk to the SMSC:
  CMG – EMI/UCP
  Nokia – CIMD
  Sema – SMS2000
  Logica – SMPP
  …
Notes: “Interface protocols for the connection of Short Message Service Centres (SMSCs) to Short Message Entitities (SMEs).”
GSM 03.39 (now ETSI TS 101 632)

## Slide 19: SIM Toolkit
Subscriber Identity Module: SIM The Smartcard in the phone
An API for communication between the phone and the SIM
Partly an API for remote management of the SIM through SMS messages.
Notes: GSM/ETSI standard.
“Security mechanisms for the SIM Application Toolkit”
GSM 02.48 (Now: ETSE TS 101 180)
“Specification of the SIM application toolkit for the Subscriber Identity Module – Mobile Equipment (SIM – ME) interface.”
GSM 11.14 (TS 101 267)

## Slide 20: SIM Toolkit Risks
Mistakes in the SIM can become remote risks.
For example insufficient protection in the SIM might allow retrieval of personal information.

## Slide 21: SMS Threats
SMS Spam
SMS Spoofing
SMS Virus

## Slide 22: SMS Spam
Getting to be like UCE
High charge call scams (“call me at xxx-VERYEXPENSIVE”)
All public SMS gateways and websites become victims.
Spammers buy bulk services from operators

## Slide 23: SMS Spoofing
Source of SMS messages is worth nothing.
Roaming capabilities of users make it impossible to filter by operators.
Only chance is for messages that stay within one SMSC/Operator.
Intercepting replies to another address is difficult.
Special case: Rogue SMSC using the Reply-Path indicator could intercept replies.

## Slide 24: SMS spoof demo
Modified sms_client
Uses EMI/UCP OT-51 message
Works on KPN, but also several foreign SMSCs
Difference with a real mobile SMS is visible with a PC.

## Slide 25: SMS Virus
Scenario: SMS is interpreted by phone and resend it self to all phone numbers in the phonebook and …
Likelihood:
  Pro: some vendors have big market shares: monoculture.
  Pro: phones will get more and more interpreting features.
  Con: zillions of versions of phones and software.

## Slide 26: SMS Phone crash demo
Modified sms_client: break the User Data Header.
Has been tested on both UCP and OIS, but should work on anything that allows specification of UDH.
Cause: broken sw in phone
Seen on 6210, 3310, 3330

## Slide 27: SMS summary
SMS is much more than just some text.
Sophisticated features are bound to open up holes (virus).
SMS very suited to bulk application (like e-mail)
Trustworthiness as bad or worse as with standard e-mail.

## Slide 28: WAP
WAP Description
WAP Protocol
WAP Infrastructure issues
WML and WMLScript

## Slide 29: What is WAP?
HTTP/HTML adjusted to small devices
Consists of a network architecture, a protocol stack and a Wireless Markup Language (WML)
Important difference from traditional Internet model is the WAP-gateway
Specifications at http://www.wapforum.org
Notes: W* Effect Considered Harmful
Rohit Khare, 4K Associates, April 9, 1999
http://www.4k-associates.com/4K-Associates/IEEE-L7-WAP-BIG.html
The Harm of the Wireless Application Protocol (WAP)
http://www.freeprotocols.org/harmOfWap/main.html
Specifically:
The WAP Trap, Mohsen Banan, Neda Communications, Inc., January 29, 2000
http://www.freeprotocols.org/wapTrap/main.pdf
The Wireless FAQ
http://www.allnetdevices.com/faq
Wireless Security Meta-FAQ
http://wap.z-y-g-o.com/wsec.html

## Slide 30: WAP network model

## Slide 31: WAP Protocol Stack

## Slide 32: WAP Protocol Stack


## Slide 33: WAP Transport Layer WDP
An adaptation layer to the bearer protocol.
Consists of
  Source and destination address and port.
  Optionally fragmentation
  WCMP
Maps to UDP for IP bearer
Notes: WAP specification WAP-200-WDP
WAP Specification WAP-202-WCMP
WAP Specification WAP-159-WDPWCMPAdapt

## Slide 34: WAP Protocol Stack


## Slide 35: WAP Security Layer WTLS
TLS adapted to the UDP-type usage by WAP.
Encryption and authentication.
Several problems identified by Markku-Juhani Saarinen:
  Weak MAC
  RSA PKCS#1 1.5
  Unauthenticated alert messages
  Plaintext leaks
Notes: WAP Specification WAP-199-WTLS
Saarinen, Markku-Juhani. "Attacks against the WAP WTLS Protocol." University of Jyväskylä, 1999
http://www.cc.jyu.fi/~mjos/wtls.pdf
Security in the WTLS
http://www.tml.hut.fi/Opinnot/Tik-110.501/1999/papers/wtls/
Vulnerabilities within the Wireless Application Protocol
Stephen Gillian
August 31, 2000
http://www.sans.org/infosecFAQ/wireless/WAP.htm

## Slide 36: WTLS
Keys generally placed in normal phone storage.
New standards emerging (WAP Identity Module [WIM]) for usage of tamper-resistent devices.
Aside from crypto problems:
  User interface attacks likely (remember SSL problems)
  WTLS terminates at WAP gateway; MITM attacks possible.
Notes: Certificate checking problem:
http://wap.z-y-g-o.com/wsec.html

## Slide 37: WAP Protocol Stack


## Slide 38: WAP Transaction layer WTP
Three classes of transactions:
  Class 0: unreliable
  Class 1: reliable without result
  Class 2: reliable with result
Does the minimum a protocol must do to create reliability.
No security elements at this layer.
Protocol not resistant to malicious attacks.
Notes: WAP Specification WAP-201-WTP

## Slide 39: WTP
PDU | Class 0 | Class 1 | Class 2
Invoke PDU | X | X | X
Result PDU |  |  | X
Ack PDU |  | X | X
Abort PDU |  | X | X

## Slide 40: WAP Protocol Stack


## Slide 41: WAP Session Layer WSP
Meant to mimic the HTTP protocol.
No mention of security in spec except for WTLS.
Distinguishes a connected and connectionless mode.
Connected mode is based on a SessionID given by the server.
Notes: WAP Specification WAP-203-WSP

## Slide 42: WAP Session layer WSP
Message types
  Connect, ConnectReply, Redirect, Disconnect
  Methods: Get, Post, Reply
  Suspend, Resume, Reply
  Push, ConfirmedPush,

## Slide 43: WAP Session layer WSP
Nothing is specified on the sessionid except that it is not reused within the lifetime of a message.
Research done in Protos (Oulu, finland) shows first implementations pretty instable.
Kannel still can’t handle large amount of connections (max threads).
Notes: Protos WSP testing
General:
http://www.ee.oulu.fi/research/ouspg/protos/
WSP specific
http://www.ee.oulu.fi/research/ouspg/protos/testing/c04/wap-wsp-request
Kannel Open Source WAP Gateway
www.kannel.3glab.org

## Slide 44: WAP Protocol Stack


## Slide 45: WAP Application Layer WAE
Notes: WAP Specification WAP-195WAEOverview
WAP Specification WAP-190WAESpec

## Slide 46: WML
WML based on XML and HTML.
Not pages of frames, but decks with cards.
Images: WBMP, WAP specific
Generally all compiled to binary by WAP gateway: Additional area of potential problems.
Notes: Wap spec. WAP-191-WML

## Slide 47: WMLScript
The WAP Javascript equivalent.
Located in separate files
Also compiled by WAP gateway
Allows automation of WML and phone functions.
Javascript bugs all over again?

## Slide 48: General WAP problems seen
Poor session support: no or limited cookie support.  encode session info in URL (not always safe.)
User identification based on WAP Gateway hack with caller ID.

## Slide 49: WAP Infrastructure issues
Attacking a dialed in phone
Spoofing another dialed in phone
Attacking the gateway

## Slide 50: WAP gateway infra
webserver
Router/Dialin
Internet
Attack on gateway

## Slide 51: Collusion attack
Rogue
webserver
Router/Dialin
Internet
Modified WML/WMLScript

## Slide 52: Attack on phone
webserver
Router/Dialin
Internet

## Slide 53: WAP 1.2
Push
  Model using a Push proxy gateway
  Dangers of user confirmation.
Wireless Telephony Application Interface (WTA & WTAI)
  Access to phone functions
  ‘Automatic’ invocation of functions from WML/WMLScript
WAP Identity Module (WIM)

## Slide 54: WAP Push
Notes: WAP Specification WAP-165-PushArchOverview
WAP Specification WAP-145-PushMessage
WAP Specification WAP-151-PPGService
WAP Specification WAP-164-PAP
WAP Specification WAP-167-ServiceInd
WAP Specification WAP-168-ServiceLoad
WAP Specification WAP-189-PushOTA

## Slide 55: WAP summary
WAP mixes too many levels.
Specs unclear in many areas concerning security sensitive issues.
WAP gateway sensitive to multiple ways of attack.
User interface interpretation very difficult on mobile devices.

## Slide 56: Future
Combining Smartcard and WTLS security; end-to-end SSL
Increased number of features (interpretation + automation)
Terrible UI
Version explosion: phones, gateways, WAP/WML.