## Slide 1: Rogue AP 101
Threat, Detection, & Defense
Notes: This is a presentation on rogue access points—what they are, what the threat is, how to detect them, and potential defense strategies. As the title indicates, this is Rogue AP 101, but assumes you already have general knowledge / understanding of wireless terminology and well-publicized insecurities.

## Slide 2: Coming up...
WiFi weakness
Rogue AP 101
Detection
Defense?
Resources
Questions
Notes: What we will be talking about today…
First, we’re going to talk about an inherent and obvious weakness with wireless networks.
Next, we will talk about what rogue APs are, how they work, why they're bad, and hopefully, even give a live demonstration of a rogue AP in action.
Then, we’re going to talk about detection of rogue access points—or what on RF Earth might be worth looking for.
Finally, we will discuss defense strategies, highlighting the pitfalls of a few, and proposing yet another one.
And after pointing you to some external resources, if there is time, we’ll open the floor up for questions.

## Slide 3: WiFi Security Soapbox…
WEP can be cracked
IPs can be spoofed
MACs can be forged
2.4 GHz can be LEGALLY jammed
“WiFi is the Wild West of Networking”
But don’t worry… there’s always a “fix” on the horizon. Right?
Notes: Excuse us why we get on the “WiFi Security Soapbox” for a minute, but for those that aren’t quite up to speed on wireless security in general…
The basic security mechanisms most wireless hardware ships with are in a word “broken”. Without getting into all of the uber proprietary security add-ons, there’s encryption that supposedly makes wireless the equivalent of a wired network (WEP – Wired Equivalent Privacy or Weak Encryption Product, your choice), there’s IP filtering, and there’s MAC access control.
Unfortunately, WEP can be cracked, IPs can be spoofed, and MACs can be forged—making these security mechanisms pretty much moot.
In addition, and what’s not commonly thought of, is the fact that communications in the 2.4 GHz spectrum (which is the spectrum our friends 802.11b and g reside), can for all intents and purposes, be LEGALLY jammed. We’re going to talk more about that in a bit.
WiFi is what I like to call, the “Wild West of Networking”. Because of some of the above insecurities, and thanks to unauthorized access being as immediate as the air you and I breathe, the users are left out there as the “pioneer prey”, and the corporations are having quite a time “settling the country”. But the similarity doesn’t stop there… because just like with the Gold Rush in 1848, the dangers, pitfalls, and worries don’t outweigh the desires. This technology is still getting deployed—and perhaps in places it shouldn’t be.
But don’t worry! There’s always a “fix” on the horizon, right? Either it’s WPA as an easy-to-install backward compatible and FREE firmware upgrade for your existing 802.11b devices, or it’s an all-Cisco and all-of-your-IT-budget EAP-SIM authentication architecture to solve all your trust issues. And if you can’t secure it, no problem there either, you can WATCH it with one of several WiFi IDS products to integrate into the IDS you’ve been diligently monitoring and dealing with every day.
Let’s hope later on in this presentation, when we talk about defense strategies, we can provide a better outlook for you…

## Slide 4: Example Setups
Wide Open
Portal w/ Password Authentication
Portal w/ Token Authentication
WEP, 802.1x to RADIUS, untrusted DMZ
WEP, 802.1x, VPN gateways, PKI, DMZ
Etc, etc, etc.
There’s a bigger problem here, that none of these security solutions solve…
Notes: So let’s talk about some example wireless network setups with varying degrees of security.
At the bottom end there’s obviously completely wide-open networks. SSID broadcasted for the Netstumbler folks, no WEP, DHCP leases doled out on demand, welcome to the corporate Intranet. How many of you are running this setup? Right. That’s what YOU think.
Then there are networks with a local portal or web redirect. Please enter your username and password, thank you, welcome to the network—but only your IP and your MAC address and only for a limited time. You see this in some nation-wide public hotspot setups actually, and we talked about why this is specifically bad at DefCon, when we demo’d Airsnarf.
There’s some folks that take it one step further and provide the redirect, but in addition to asking for a username, the password is a one-time generated token, like SecurID or similar. Not secure either, by the way.
If we start adding on the layers of security, we can come up with more setups that are ever-complex. Toss in WEP, require 802.1x, call the wireless network untrusted, toss in a VPN edge or gateway device behind the AP, require certificates, mutual authentication, etc., etc., etc.
There’s a bigger problem here, that none of these security solutions, in all their glory and cost, will solve…

## Slide 5: Why pick the lock, when you can ask for, and be given, the KEY?
Notes: From the attackers perspective, determined adversary or 13-year-old prankster, the simple question is…
Why pick the lock, when you can ask for, and be given, the KEY?

## Slide 6
Access Point
SSID: “goodguy”
SSID: “badguy”
Stronger or Closer
Access Point
“ANY”
Wi-Fi Card
SSID:
“goodguy”
“badguy”
Notes: Let’s say we have an access point with an SSID of “goodguy”. If a wireless client with their SSID set to “ANY” enters the range of the access point “goodguy”, they will associate to “goodguy” and the client’s SSID will effectively become “goodguy”.
However, if another access point with an SSID of “badguy” enters the picture, and in relation to the wireless client, “badguy” is either physically closer or it’s signal is stronger than “goodguy”, then there is the potential for the client to re-associate to the closer and stronger access point “badguy”, and the client’s SSID will effectively become “badguy”.
It is possible for the mis-association pictured here to happen without the user’s knowledge. Even worse, the badguy access point here could just have easily set its SSID to “goodguy”, making it even easier for the mis-association to occur, and making it that much more difficult for the user to detect.
Such is the threat of rogue APs in wireless environments.

## Slide 7: Rogue APs?
Rogue AP = an unauthorized access point
Traditional
  corporate back-doors
  corporate espionage
Hotspots OR Corporate Environments
  DoS
  theft of user credentials
  AP “cloning”
Notes: What is a rogue AP? A rogue AP is an unauthorized access point.
Traditionally, in a closed network, this is an access point that allows unauthorized entry into the network. This can be a user standing up their own wireless access point for the sake of convenience, attached to the corporate network, providing an unintentional back-door. Or this can be a competing company one floor up slipping 20 bucks to a janitor for dropping an AP on your LAN so they can perform a bit of corporate espionage by pointing an antenna at their floor / your ceiling. Either way, it’s a network security officer’s nightmare.
Another obvious use for rogue APs is open or public networks. This can be as hands-off as dropping an overpowered AP in the midst of a public network with a redirect to a splash page stating, “Save the Moose!” , thereby creating a denial of service. Or this can be as involved as walking around in a coffee house with a wireless-capable PDA in AP mode duping users into giving up their hotspot usernames and passwords.
As always, users are the simple way into a network. Wireless or not.
But wait, here’s a new twist to using rogue APs for network penetration…

## Slide 8
Inverse Wardriving v. (gnivirdraw)
1. A rogue AP looking for “WiFi suckers”.
2. And you thought a user dual-homed with a modem was bad… ?
Notes: What happens if we wardrive, not with the intention of finding wireless access points, but with the intention of finding wireless CLIENTS?
Let’s call it “Inverse Wardriving”, or “Gniverdraw” if you’re so inclined.
Basically, we have a user who is hard-wired to the corporate Intranet at their workstation, which in this case is really a laptop in the docking station which, oh by the way, happens to have a PCMCIA or built-in even, WiFi card. It’s just happily sitting there in “ANY” or “default” mode looking for access points to associate to, setup for DHCP and everything.
<click>In comes our rogue AP on wheels, the inverse wardriver, and they are just blasting out juicy signal <click> for any client to grab ahold of.
And when we do get a client, and let’s just assume for the sake of this presentation because we know it would never happen in the real world, the client happens to be an unpatched Windows machine. What do we do with that Windows machine? Well the current trend happens to be worm activity, so let’s go ahead and deliver one of those badboys. <click>
Of course, the rest of this scenario couldn’t happen in the real world either… <click> <click>
But the point here is that we’re not exploiting a wireless network, per se, we’re exploiting wireless clients. We’re hardly even exploiting the USER in this case, we’re simply exploiting the stupid desires of the wireless client hardware to be a part of a network, “ANY” network. And you thought a user dual-homed with a MODEM was bad?

## Slide 9: Rogue AP Mechanics
“Create a competing wireless network.”
AP can be actual AP or HostAP
Create or modify captive portal behind AP
Redirect users to “splash” page
DoS or theft of user credentials, or WORSE
Bold attacker will visit ground zero.
Not-so-bold will drive-by with an amp.
Notes: So what are the mechanics behind a rogue access point?
Basically, the idea is to simply create a competing wireless network. A rogue AP is essentially a wireless network of its own, but with a purpose other than providing legitimate service to the Intranet. Instead, the main purpose is to steal credentials from unsuspecting users and use those credentials for illegitimate access to the target legitimate network.
The AP component of a rogue AP can be an actual access point or a simple wireless card running HostAP.
Off the backend of the AP, an attacker can create a captive portal, which accepts DNS and web queries, but redirects all users to a “splash” page of some sort. Depending on how open the wireless network is to begin with, we can simply sit as a “man in the middle” acting as a “repeater” of sorts, brokering wireless connections from the rogue wireless network, to the legitimate wireless network.
An attacker can simply deny service to all users or go so far as to steal usernames and passwords—perhaps even provide no interaction with the user and simply make the user a vector for some infection into the wired network.
If the attacker is bold, they can do this intermittently while using the network. One day, they are a legitimate user, the next, a rogue AP—yet another new insider threat for you.
A big antenna and amp can facilitate a drive-by rogue AP. Let’s see an example rogue AP setup in action.

## Slide 10: Airsnarf
Nothing special
Simplifies HostAP, httpd, dhcpd, Net::DNS, and iptables setup
Simple example rogue AP
Demonstration
Notes: Airsnarf is a rogue AP setup utility we will now demonstrate.
Simply put, it’s just a shell script that integrates and sets up several fairly standard Linux utilities to create a rogue access point, specifically:
HostAP for AP functionality, httpd to serve up the splash page, dhcpd to give out IPs/DNS/gateway, a simple Perl-based Net::DNS::Nameserver DNS redirect, and iptables to funnel all the DNS requests the gateway sees to a local port
All of these Linux utilities are publicly available.
(Demonstration)

## Slide 11: What’s the big deal?
Regardless of WiFi security infrastructure, you ARE “vulnerable” to this
Users WILL give up credentials, WEP keys, you name it
If you’ve got SSO, doh!
Physically finding the rogue AP / client can be a challenge
This is more of a traditional social engineering problem than a technical vulnerability—what’s the “patch”?

## Slide 12: Detection
ANY wireless activity (if policy is no WiFi)
Duplicate SSIDs
Different / mismatching MACs
Interference / SNR spikes
Association requests
More…

## Slide 13: Client Defense Strategies
Local AP awareness
User education
One-time authentication mechanisms
Application authentication
No WiFi? No WiFi connected to Intranet?
A defense kit for wireless users…? Sort of a ZoneAlarm for WiFi?
Notes: For those people operating public hotspots looking for defense strategies…
Being aware of what APs are running in your local environment MIGHT help. Watch out for fake AP generation that sends you on a wild goose chase, though.
User education could be key. Being up front with wireless users and telling them what to be on the lookout for. SSL only works if people make sure to check for that little lock! The same goes for your VPN software, specifically, it’s policies. If the local VPN security policy on the user’s computer says anything 10.0.0.x must be encrypted, but the rogue AP uses 192.168.1.x for its address scheme, your VPN-over-wireless-on-demand solution just FAILED.
A one-time authentication mechanism may seem like a good idea, but don’t make its entry via a webpage! Your SecurID generated number does you no good if I can just ask a user for it, and immediately use all of their login credentials to access the same legitimate network (perhaps through I different entry point even), within 10-15 seconds of their stolen login.
Application authentication. Assume the wireless network security will be defeated but provide an otherwise useless network on the other side via application authentication requirements. 802.1x isn’t just for wireless. But beware of tying wireless authentication to your single-sign-on infrastructure! One snagged WiFi login = access to everything?
Here’s a thought—no WiFi. So instead of weeding out the bad WiFi, you can just call all of it bad via policy. Or, just provide wireless for the Internet’s sake not your Intranet’s sake.
What if there were software for wireless users, a sort of defense kit they could run on their laptops, like ZoneAlarm for WiFi, where basically, signs or indications of a rogue AP would provide popups to the user indicating new threat level? Different IP scheme detected? Alarm. New or duplicate SSID detected? Alarm. Re-association to the AP? Alarm. Strange SNR spike? Alarm. However, the question is, would users even care?

## Slide 14: A Real Fix - 802.1x
Link layer authentication
  Port Based with extensible auth
A real layer 2 solution
  Everything at a higher level fails somehow
Need an EAP method that supports bi-directional authentication
  Eg: EAP-TTLS, etc..
To be included in 802.11i

## Slide 15: Links that make you go “hmmm”
Airsnarf - http://airsnarf.shmoo.com
ISS Wireless LAN Security FAQ - http://www.iss.net/wireless/WLAN_FAQ.php
SANS Wireless Reading Room - http://www.sans.org/rr/catindex.php?cat_id=68
SAFE: Wireless LAN Security in Depth - http://www.cisco.com/go/safe
Google - http://www.google.com/search?q=wireless+security
Notes: Here are some links.

## Slide 16: Questions?
Notes: Questions?