## Slide 1
Jim Harrison
Tom Shinder
  Concepts and Functional Use
Microsoft Internet Security and Acceleration Server 2000
Notes: This deck presents a functional description of ISA Server, including deployment, management and troubleshooting.
Intended Audience: Deployment planners, Datacenter Admins
Technical Level: Moderate

## Slide 2: Agenda
Introduction - Agenda
Deployment scenarios
  Enterprise Arrays
  Standalone
ISA clients
  SecureNAT
  Firewall
  Web proxy
Web / Server Publishing
Troubleshooting techniques
  Reading the logs (and understanding them)
  Interpreting the Event log entries
Notes: Welcome to Black 2002!
Today, we’re going to discuss ISA in a way that may seem strange to some of you; all the marketing and “ain’t it kewl” dog and pony show is out.
Instead, we’ll present you some of our own experiences and offer you some real-world configuration and troubleshooting techniques

## Slide 3: Deployment Scenarios
Secure internetworking with a scalable, multi-layer firewall
Fast access with a scalable, high performance Web cache
Enterprise Arrays
Standalone
Notes: <header>
<date/time>
Microsoft ISA Server includes has 4 major capabilities:
Security –Enterprise firewall
-securely routes requests and responses between the Internet and client computers on the internal network.
-Firewalls usually separate a protected ‘internal’ network from the ‘external’ network I.e. a LAN connected to the Internet via Firewall.
-Firewalls can help defend your network from external hackers, unauthorized access and virus attacks; does this by filtering/analyzing traffic as it passes through the firewall computer.
Performance – ISA provides high performance Web Cache Server
-Web Cache Servers speed up web site access performance for browser clients by storing frequently requested Internet sites so that the objects can be quickly accessed by clients directly from the ISA Server computer, rather than from the Internet.
-Web caches can be used to speed up performance for internal user accessing the internet or external clients accessing your web server.
Management – The Firewall provides Secure connections to the Internet; the Cache Server provides the Fast Internet experience- ISA Server provides both benefits with integrated management. Unified management that simplifies network complexity and provides consistent control over your internet access
Extensible – a customizable platform that can be extended through APIs and SDKs. For example, the entire interface is scriptable COM objects. You can customize the interface or add additional security filters.
Competitive Advantage
ISA Server provides the robust features required of an enterprise Firewall to provide excellent security for your network. ISA also provides fast web caching features that help improve Web access performance for internal clients as well as fast e-commerce response for external customers.
The integrated management provides organizations with a more secure environment by applying the same access policies to the firewall and the cache; ISA lowers cost by having to learn and train for a single management interface; minimize network complexity by have an integrated system of Internet access, security and web performance.
Other vendor products are focused on a single aspect and require you to learn multiple technologies and management consoles. With ISA Server, you can choose to deploy firewall and caching on separate computers but the setup and management is consistent. In addition, ISA Server takes advantage of Windows 2000 features such as QoS, VPN, advanced authentication, NAT, Active Directory and more.

## Slide 4: Enterprise Array
Centralized Domain Policy
All Members in Same Active Directory Site
Active Directory Required
Multiple Policies
“Array Level” control allowed
Distributed Caching
ISA Enterprise Version ONLY
ISA Server Objects Added to Active Directory
Notes: Centralized Domain Policy
An Enterprise Array allows you to configure a centralized access policies that can be applied to multiple arrays in an organization. Enterprise Policies allow you to set what is the maximum level of access allowed for network clients behind the array that has the enterprise policy applied. All ALLOW rules must be created at the enterprise policy level for Enterprise Arrays.
All Members in the Same Active Directory Site
All Array members must belong to the same Active Directory Domain and Site. Active Directory Sites are based on network IDs.
Active Directory Required
You must have Active Directory installed and running in your organization to create Enterprise Arrays. Enterprise Arrays cannot be created if the ISA Servers are members of an Windows NT 4.0 domain.
Multiple Policies
You can create multiple Enterprise Policies to meet the requirements of different arrays in your organization. You may want to apply one Enterprise Policy to the California sites and a different Enterprise Policy to the Texas sites. A single Enterprise Policy can be applied to multiple arrays, or you can apply a different Enterprise Policy to each array. The key of Enterprise Policies is that that they allow centralized control over the maximum level of access into and out of the ISA Array members.
Array Level Control Allowed
Although Enterprise Policies allow centralized control over the mximum level of access, you can create Enterprise Policies that allow find tuning at the array level. Note that an array administrator can only add further restrictions to the access policy. The array level administrator cannot add ALLOW rules. Enterprise Policy can be configured to allow Array Level publishing rules.
Distributed Caching
Unlike Proxy 2.0, you must have all array members be members of an Active Directory domain and join the enterprise array to take advantage of distributed caching. For larger organizations, distributed caching can significantly speed up access for internal network clients, and reduce bandwidth required on the external interface.
ISA Server Enterprise Version Only
You must have ISA Server Enterprise version to create an Enterprise Array. ISA Server Standard version does not support array configuration. This is another significant difference from Proxy Server 2.0.
ISA Server Objects added to Active Directory
The Active Directory must be ‘initialized’ with ISA Server related objects added to the Active Directory. If communications between the ISA Server array members and the Active Directory are interrupted, Enterprise Policies and array members will not start propertly.

## Slide 5: Standalone ISA Server
Does not support Enterprise Arrays
Active Directory not required
Member of AD or NT domain
No Distributed Caching
Hierarchical Caching Available
Easiest to configure and manage
Suitable for small and medium biz
Beef up the hardware
Notes: Does not support Enterprise Arrays
Stand-alone ISA Servers are not members of an enterprise array. Policies are configured on a per stand-alone server basis.
Active Directory not Required
Stand-alone ISA Server computers do not need to be a member of an Active Directory domain. These machines can be members of a Windows NT 4.0 domain, or ever be installed as stand-alone servers without domain membership. If you install the machine as a stand-alone server that is not a member of any domain, the only accounts database that you can use for access control is the local SAM. Note that if you use the stand-alone ISA Server as a VPN server, you can use RADIUS authentication to authenticate against a Windows 2000 Active Directory domain.
Member of Active Directory or NT Domain
The stand-alone ISA Server can be a member of an Active Directory or NT domain. The ISA Server can take advantage of trust relationships you configure for your internal network domains as well.
No Distributed Caching
Since the stand-alone ISA Server cannot be a member of an Array, it cannot perform distributed caching. However, the stand-alone ISA Server can be chained to upstream ISA Servers to create a hierarchical array. The hierarchical array allows the downstream ISA Servers to take advantage of cached contents on upstream ISA Servers and arrays.
Hierarchical Caching Array Available
When the downstream ISA Server does not have information cached, it can forward the request to an upstream ISA Server. If the upstream ISA Server has the content in cache, it will return this content without sending the requests to the Internet server. This improves client-side performance and reduces the overall bandwidth required on the common Internet interface.
Easiest to configure and manage
Stand-alone ISA Server are the easiest to configure and manage because you don’t have to think about the interactions between Array and Enteprise level policies. If you don’t have experience with enterprise level policies, there will be a bit of a learning curve before you get all the bugs worked out!
Suitable for Small and Medium Sized Biz
Businesses that are small enough not to require centralized management of access policies do not require an array. A single stand-alone ISA Server can support a remarkable number of requests. And because much of the cache is held in RAM, the latency for retrieving cached content is very low.
Beef up the Hardware
While always the case, a single stand-alone ISA Server should have its hardware maximized. You can support thousands of users with a single stand-alone ISA Server with 4 GB RAM and a SMP configuration.

## Slide 6: ISA Server Clients
Web proxy
  CERN-compatible proxy server
  HTTP, HTTPS, FTP, Gopher protocols only
  OS-independent
SecureNAT
  Uses ISA as a router
  Simple protocols only
  OS-independent
Firewall
  Winsock proxy (supports Proxy 2 client)
  Complex protocols
  Windows 9x and later
Notes: ISA server provides support for client requests in three ways:
CERN-compatible HTTP, HTTPS, FTP and Gopher proxy
  Only allows HTTP, HTTPS, FTP (download only) and Gopher protocols (Cache mode GOTCHA)
  OS is unimportant; only the browser or app capabilities matter; must comply with CERN proxy request requirements
Very basic NAT and routing functions for non-proxy clients
  No complex (negotiated) protocols; single-protocol traffic only
  Requires separate DNS functionality for non-web protocols if using the HTTP redirector
  Only client that can PPTP through the firewall
  Only client that can be server-published
Winsock Layered service provider
  Proxy-2 Winsock proxy service-compatible
  Allows nearly any protocol (as defined)
  Offers very granular configuration of LSP behavior on a per-application basis
  Supports Proxy-2 server publishing technique
Name Resolution – The correct IP settings for your ISA server are absolutely critical. At the very least, you have to provide a DNS server for ISA to resolve external FQDN on behalf of Web Proxy and Firewall clients, and you should provide an internal DNS server for the internal network as well. ISA lives on a W2K server and W2K prefers DNS to any other name resolution scheme. Relying on WINS or NetBIOS broadcast name resolution (yuck!) is a sure recipe for intermittent troubles later on.
  ISA provides for its own DNS lookups by creating a DNS Lookup Packet Filter. Make sure you leave this enabled, or ISA may not resolve external names correctly.

## Slide 7: Client support
Built-in DNS cache for Web & Firewall clients
  Eases DNS requirements in simple deployments
  Can be disabled via registry if desired
Force web proxy for SecureNAT & Firewall clients via HTTP Redirector
  Can help enforce authenticated access policies
User Authentication for Web & Firewall clients
  Provides for user / group access policies
  Basic, Integrated and W2K AD Digest authentication is supported
Outbound PPTP for SecureNAT clients
Notes: Web Proxy and Firewall DNS cache:
The Web Proxy and Firewall services provide very basic DNS “services” that are totally dependent on the DNS settings made in the ISA IP configurations. They will resolve FQDN requests for Web and Firewall clients using the DNS servers as defined in the ISA IP configuration. Errors here will make name resolution an unholy mess for your Web and Firewall clients. Make sure your ISA server can resolve names properly and quickly!
The really interesting part is that they have the unique ability to totally ignore the TTL normally associated with the DNS record received from a DNS server. By default, all records held by the Web Proxy and Firewall DNS caches have a TTL of 6 hours, regardless of the actual TTL associated with the record! Needless to say, this can wreak havoc on your client’s name resolution; not to mention any DNS-related testing you may be performing.
What can we do about this? Plenty. There are two entries in the registry (or Active Directory for Enterprise arrays) for each service in each array that define the size of the DNS cache and the default record TTL. They are:
Web Proxy:
HKLM\SOFTWARE\Microsoft\Fpc\Arrays\{Array GUID}\ArrayPolicy\WebProxy
"msFPCDnsCacheSize"=dword:00000bb8
"msFPCDnsCacheTtl"=dword:00005460
Firewall:
HKLM\SOFTWARE\Microsoft\Fpc\Arrays\{Array GUID}\ArrayPolicy\Proxy-WSP
"msFPCDnsCacheSize"=dword:00000bb8
"msFPCDnsCacheTtl"=dword:00005460
Note: for Enterprise Arrays, you have to use Active Directory Users and Computers in Advanced view mode, and drill down to System, Microsoft, FPC, Arrays, {Array GUID}, Array policy, etc…

## Slide 8: Client Access Policy
  Site and Content Rules
  Protocol Rules
  IP Packet Filters
Notes: Site & Content Rules - This is where we control the content that passes through ISA. By default, ISA creates a single “Allow rule” that allows any request to pass. You can play all sorts of allow / deny games in here, but be very careful; you can create conflicting rules that will leave your ISA totally blocked
Protocol Rules – This is just one of many areas of control within the mind of ISA, but the most easily overlooked. At the bare minimum, you have to allow HTTP and HTTPS in order to have web access for your LAT hosts. There are many more protocols, but without those, you can’t browse the web. You can see that I’ve defined a great many protocol rules for my LAT hosts to use; some of which are custom definitions.
IP Packet Filters – These provide access to / from apps and services located either on the ISA itself or to a third-leg DMZ. The only notable exception is the use of packet filters for SecureNAT PPTP through ISA
Generally speaking, any policy element that goes by the name Rule can make use of any of the elements of Policy Elements

## Slide 9: WPAD Configuration
Auto Discovery listener
This is the heart and soul of WPAD and WSPAD functionality
Notes: This is one of the great heartaches for folks trying to run IIS and ISA on the same server, even when they limit IIS to the internal IPs. Since no two applications or services may claim the same TCP/IP resources, it becomes a race and the loser gets denied. This is also the source of the dreaded WPAD functionality. Click on Auto Discovery and you’ll see the default settings
If you don’t need or want Auto Discovery, then just uncheck Publish automatic discovery information. That will free up port 80 on the internal IPs.
Note that ISA can function as a Web proxy server using only one NIC. The only ISA operating mode that supports single-NIC operation is Cache Mode.
Also note that changing this port from its default value of 80 will break WPAD and WSPAD unless DHCP WPAD support is in place and correctly configured.
Both the Web proxy and Firewall clients use the Auto Discovery listener to gather configuration data
Note that disabling this feature does not affect the Web and Firewall client’s ability to make http://<servername>/wpad.dat and http://<servername>/wspad.dat calls, respectively

## Slide 10: Outgoing Web Requests
Outgoing Web Requests
In order for ISA to function as a Web proxy, the Outbound Web Requests Listener has to be properly configured.
Notes: To see and change this setup, open the ISA Management MMC and drill down to Servers and Arrays, <ServerName>. Right-click <ServerName> and select Properties. Click the Outgoing Web Requests tab and you’ll be rewarded with something like this:
By default, ISA enables the proxy service on all of the ISA internal IPs at port 8080 (including 127.0.0.1; the localhost IP), regardless of operating (Firewall, Integrated, Cache) mode. That port is used because the ISA Auto Discovery functionality operates at port 80 on all of the ISA internal IPs. To disable the Outgoing Web Requests listener, simply select Configure listeners individually per IP address and don’t select any IPs to listen on.
Note that access via the Outbound Web request listener is controlled by site and content rules and their associated data points from Policy Elements. It is literally impossible for the outgoing listener to service external requests for external sites.
Authentication can be enabled on a per-IP basis (if selected) and enforced here as well.

## Slide 11: HTTP Redirector
Controls firewall and SecureNAT client web access
Notes: Redirect to local Web Proxy service – this allows you to force the firewall and secureNAT clients to use the filtering and routing functionality of the web proxy service. It also has the side effect of limiting Web Proxy request capability if you require user authentication for web requests, since user credentials are lost here. All web logs for these requests will have “127.0.0.1” in the cs-ip field.
  If the local service is unavailable, redirect requests to requested web server – this allows secureNAT and Firewall clients to reach the Internet in the event that the local Web Proxy service is unresponsive
Send to requested web server – send secureNAT and firewall client requests directly to the destination server
Reject HTTP requests from Firewall and SecureNAT clients – just as it says; any web request from a SecureNAT or firewall client will be rejected. This setting is useful if you want to limit the web traffic to the Web Proxy service.

## Slide 12: Web Proxy Clients
  Application or browser proxy settings use <ISAServer>:8080
  All ISA operating modes
  Non-MS clients if CERN-proxy compliant
  ISA Auto-detect supports IE5 and later only
  Protocols
    HTTP, HTTPS, FTP (download), Gopher
  No secondary protocols
  Basic, Integrated, Digest Authentication
  DNS C.O.D.
Notes: Any application or browser that is capable of making an http proxy request for a supported protocol can be served by an ISA server
Web proxy services are available in Cache, Integrated and Firewall modes
Not OS-specific, though logs might hold interesting data for non-MS systems
WPAD only supports IE5 and later; other apps can be “educated” by analyzing the data from the file obtained with http://<isaserver>/wpad.dat or http://<isaserver>/array.dll?Get.Routing.Script
Only FTP is supported for secondary protocols because of the FTP application filter
Inbound authentication can only be Basic; NTLM-based auth cannot pass inbound through ISA
DNS cache-of-death can cause many seemingly intermittent issues because of the default 6-hour TTL for all records
  HKLM\SOFTWARE\Microsoft\Fpc\Arrays\{Array GUID}\ArrayPolicy\WebProxy
  "msFPCDnsCacheSize"=dword:00000bb8 (3000 bytes)
  "msFPCDnsCacheTtl"=dword:00005460 (21600 seconds, or 6 hours)

## Slide 13: Browser configuration for WPAD
Notes: Automatically detect settings – This is completely dependent on the WPAD support available in the host network; if the data can’t be obtained, the browser acts like a SecureNAT client
Use automatic configuration script – The URL entered here should point to a server (ISA or WEB) that can provide a configuration script for the browser. If pointing to an ISA or Proxy 2 server, the URL must always end with “/array.dll?Get.Routing.Script”.
Use a proxy server for your LAN (these settings will not apply to dial-up or VPN connections) – this is the step of last resort when all other configuration choices fail. Pay particular attention to the disclaimer here; IE makes a very clear distinction between LAN and dial-up connections.

## Slide 14: RAS browser settings
Notes: In the “Settings” for each dial-up connection in IE, you have the option of defining a different proxy than the global IE setting.
This allows you to use the proxy at work while connected, then switch back without requiring any user action.
WPAD also works for RAS clients if the DHCP <proxy?> is configured properly at the RAS server. This allows the dial-in user to get the correct DHCP and DNS server settings required for WPAD operation.
Note the availability of the user alias, password and domain. This provides credentials for IE to impersonate in the RAS network. While it’s very convenient for the user, it’s a potential security risk in that the user’s credentials are persisted on their local host even when they’re disconnected.

## Slide 15: ISA Configuration for SecureNAT Clients
Notes: Enable packet filtering – this is the heart and soul of ISA’s stateful packet filtering. If you turn this off, all protocol rules and packet filters are disabled and traffic will flow to and from ISA without hinderance
  Enable intrusion detection – this enables the filters found in the Intrusion Detection tab.
  Enable IP routing performs several functions;
    It allows fast “kernel mode pumping” of IP packets for more efficient data transfer through ISA
    It allows secureNAT ICMP traffic to reach an Internet host
    It allows SecureNAT clients to use PPTP through the ISA server (PPTP tab).
    If this is enabled and Enable packet filtering is disabled, ISA becomes a dumb router; not even as functional as RRAS.

## Slide 16: SecureNat Clients
  Host computer uses ISA as its default route
  Only Firewall and Integrated modes
  Non-MS clients
  No ISA Auto-detect capabilities
  Can use any simple protocol that is defined and allowed
  No user Authentication
  Requires separate DNS structure
Notes: Client host must either have ISA default internal IP as its default gateway or have ISA as the last default route in the router chain
ISA Cache mode does not support secureNAT, since there are no “routing” capabilities without the Firewall service
Not OS-specific, though logs might hold interesting data for non-MS systems
No such concept as secureNAT auto-detection
Even with the FTP application filter, secureNAT clients can’t use PASV FTP
Clients requests do not carry authentication
Must have a DNS resovler in the IP settings

## Slide 17: ISA Configuration for Firewall Clients
Application Settings
ISA Firewall client functionality can be configured on a per-application, per-host basis for very granular control over client functionality
Notes: The ISA Firewall client software saves these and other ISA configuration options (LAT, LDT) in two local files called mspclnt.ini and msplat.ini. Together, they determine how an application or service interacts with the ISA server
The Firewall client can obtain ISA auto configuration using the same means as IE; through WPAD. Additionally, a DHCP Inform request will return the DHCP scope option 252 if it figured.
If the Firewall client has no DHCP facilities, it will use :
  Nearly the same WPAD call to ISA: http://wpad/wspad.dat. Note that the file requested is different. Wpad.dat is a Jscript that IE uses to configure itself, while wspad.dat is the larger portion of the data contained in mspclnt.ini.
  the connection specified in the initial copy of mspclnt.ini to refresh its settings
..once connected to the ISA server, it will also make a call to TCP-1745 for a more detailed data set that also includes the LAT.

## Slide 18: Firewall Clients
  ISA or Proxy 2 client software is installed on the LAT host
  Firewall and Integrated modes only
  Non-MS clients are not supported
  Auto-detect works for ISA and Proxy 2
  Protocols; any defined and allowed
  Allows secondary protocols
  Client Authentication uses interactive logon credentials
  DNS C.O.D.
Notes: FW client software must be installed
DNS cache-of-death exists here, too
  HKLM\SOFTWARE\Microsoft\Fpc\Arrays\{Array GUID}\ArrayPolicy\Proxy-WSP
  "msFPCDnsCacheSize"=dword:00000bb8 (3000 bytes)
  "msFPCDnsCacheTtl"=dword:00005460 (21600 seconds, or 6 hours)

## Slide 19: Web and Server publishing
Web Publishing
Server Publishing
Packet Filtering
Notes: Publishing allows Internet clients to access resources on the internal network.
Web Publishing
Web Publishing allows you to publish HTTP and FTP sites by taking advantage of application layer aware Web Proxy service. Web Publishing allows you to take advantage of many features not available with Server Publishing Rules
Server Publishing
Server Publishing rules provide for the most part simple port forwarding. Packets that arriving to a particular port on the external interface IP address of the ISA Server are forwarded to the internal network server that you’ve configured them to be forwarded to in the Server Publishing Rules.
Packet Filtering
The poorest of the Poor Man’s publishing rules. This method just opens up ports on the external interface of the ISA Server and allows Internet clients direct access to these ports on the external interface of the ISA Server. Not recommended.

## Slide 20: Web Publishing
Single IP Address for Multiple Sites
Access Control at Listener
Examines HTTP Header
Port Redirection
SSL Bridging of HTTP requests
HTTP Bridging of SSL requests
Caching of inbound requests
Plug in Support
Notes: Single IP Address for Multiple Sites
Web Proxy services listens for incoming requests using the Incoming Web Requests listener configuration. If you have multiple addresses on the external interface of the ISA Server, you can configure multiple Incoming Web Requests listeners. You can have a single IP address on the external interface and publish multiple internal sites and servers. Different authentication requirements can be place on different listeners.
Access Control at Listener
Each Incoming Web Request listener can be configured to require a certain type of access control. If you configure multiple Incoming Web Requests listeners, one can require client certificate authentication, while another might require integrated authentication and another may require no authentication at all. Requests can be authenticated at the Listener and/or the internal Web server.
Examines the HTTP Header
Because the Incoming Web Requests listener works with the Web Proxy service, requests coming into the listener can be examined by the Web Proxy service. The Web Proxy service examines the contents of the HTTP header and makes decisions regarding how to forward the request based on matches between the site noted in the header and a Destination Set included in a Web Publishing Rule.
Port Redirection
One feature only available with Web Publishing Rules is the ability to perform port redirection. Requests can come in only any port you configure the listener to listen on, and can be redirected to another port number on the internal network server. Note that this only works for HTTP(S) and FTP requests, which are handled by the Web Proxy service. Server Publishing does NOT allow for port redirection, just forwarding.
SSL Bridging of HTTP Requests
Web Publishing Rules allow you to forward HTTP requests as SSL/TLS requests. This isn’t much use unless you trust the Internet more than you do the network inside the ISA Server
HTTP Bridging of SSL Requests
You can significantly improve performance by bridging SSL requests as HTTPS requests. In this case, the SSL tunnel is terminated at the external interface of the ISA Server and forwarded to the internal Web server as an HTTP request. The Web site’s certificate is installed on the ISA Server and the ISA Server impersonates the internal network Web server.
Caching of Inbound Requests
Since the Incoming Web Requests listeners forward to the Web Proxy service, all requests made by via Web Publishing rules are cached on the ISA Server itself. This takes the heat off the internal network Web Server and reduces traffic on the internal network because the requests can be serviced from the ISA Server cache, which keeps information in RAM and therefore can potentially respond much more quickly than a busy Web Server on the internal network.
Plug in Support
The Web Proxy service can take advantage of ISAPI plug in’s. The tools used to secure Web Servers, such as the URLScan tool. Work is in progress to allow you to integrate URLScan with ISA Server.

## Slide 21: Server Publishing
Publish All Services
Access Control – Client Address Sets
No Port Redirection
Can use Application Filters
One IP Address per Service
Watch out for contention!
Notes: Publish All Services
Server Publishing Rules allow you to make all services on the internal network available to external network users. Most services can be published using simple Protocol Definitions that have the primary connection configured for inbound access. More complex protocols, such as Exchange RPC, require the aid of the Application Filters to manage the connections.
Access Control – Client Address Sets
In contrast to the Web Proxy’s Incoming Web Requests listener that can authenticate users at the ISA Server’s interface itself, Server Publishing Rules can only control access using Client Address Sets, which are collections of IP addresses. Any other type of authentication must be performed on the internal server itself.
No Port Redirection
In contrast to the Web Proxy service’s Incoming Web Requests listener that can redirect requests to an alternate port, Server Publishing Rules on only forward to the same port that it received the request on. For example, if a request came on in on TCP 25 at the external interface of the ISA Server, it will be forwarded to TCP 25 on the internal network server. If you need port redirection, you will need a 3rd party product add-in such as Surrogate Sockets.
Can use Application Filters
Server Publishing Rules depend on Protocol Definitions to do almost all the work. However, smart Application Filters can be used to help out otherwise dumb Server Publishing Rules using inbound Protocol Definitions. Examples of built-in Application Filters that can be used to support Server Publishing Rules include the FTP Access Application Filter and the Exchange RPC Application Filter. These filters will examine the data portions of the packets accepted by FTP and Exchange RPC publishing rules and allow access for clients requiring these more complex protocols.
One IP Address Per Service
In contrast to the Web Proxy service’s Incoming Web Requests listener that lets you publish multiple servers using a single IP address on the internal interface of the ISA Server, Server Publishing Rules let you publish a particular service only once per IP address. For example, if you have a single IP address on the external interface of the ISA Server, you can only create a single SMTP Server Publishing Rule and publish only one SMTP server on your internal network. If you need to publish a second SMTP server, you will need to bind a second IP address to the external interface of the ISA Server.
Watch out for contention!
While an issue for Web Publishing, port contention becomes an even better issue for Server Publishing Rules by virtue of the fact that Server Publishing Rules supports more services. In order to publish an service, you must allow the ISA Server to listen on that’s services port number. If there is also a service running on the ISA Server that requires the use of the same port, the Server Publishing Rule will fail. This most common reason for this is that IIS services are running on the ISA Server. If you allow the IIS SMTP service to run, it will listen on all IP addresses on the server and will contend with an SMTP Server Publishing Rule. This will prevent the SMTP Server publishing rule from working.

## Slide 22: Packet Filtering
Not true Server Publishing
Used for DMZ Servers
Direct Access to Servers
Very Limited Access Control
Not Recommend for Services on ISA Server
Primarily for outbound access to non-TCP/UDP Protocols
Notes: Not true Server Publishing
You can run services, such as SMTP or FTP, by creating packet filters that open up their ports on the external interface of the ISA Server. This is akin to placing a server directly on the Internet and closing off all ports except those allowed by the packet filters. Biggest problem with this approach is that you’re placing network services on the ISA Server itself.
Use for DMZ Servers/Direct Access to Servers
Packet Filter must be used to ‘publish’ servers on a DMZ segment on a trihomed ISA Server. When you configured a DMZ segment on a trihomed ISA Server, the DMZ segment must have public addresses. The only way to allow inbound and outbound access to and from the DMZ segment on a trihomed ISA Server is to create packet filters. Again, there is no application layer filtering or exposure of the data portion of the packets to any service or application filter on the ISA Server. The ISA Server acts as a router to and from the DMZ segment.
Very Limited Access Control
You can limit access for a particular packet filter based on IP address, group of IP addresses or network ID. There is no user/group access control and you cannot use Client Address Sets. The ISA Server acts as a very simple packet filtering router when using packet filters to allow access to services on the ISA Server itself or on a public network ID DMZ segment.
Not Recommended for Services on the ISA Server
Its not recommend that you run any server services on the ISA Server itself except for the ISA Server services. Each addition service provides a potential vector of attack on the ISA Server. If the ISA Server is compromised, it has the potential for allow further compromise or your network and create a DoS condition where no inbound or outbound traffic will be possible.
Primarily used for Outbound Access for non-TCP/UDP Protocols
Packet filters must be used to allow outbound access for non-TCP/UDP protocols because you cannot create Protocol Definitions for any other type of protocol. Example of non-TCP/UDP protocols are GRE (IP Protocol 47) which is required by clients needing access to outbound PPTP, and ICMP which is required if you need to allow internal SecureNAT clients to ping and tracert. Note that ISA Server does not support L2TP/IPSec VPN tunnel passthrough.

## Slide 23: Troubleshooting
Use the isainfo script
Log analysis
W2K troubleshooting techniques
Network troubleshooting techniques
Notes: ISA troubleshooting is based on sound Windows and networking problem resolution techniques
  Just because it’s an ISA server doesn’t mean it’s a totally different beast; W2K still forms the main underpinnings
ISAINFO.VBS; Props to Chad Mosman for his initial and continuing efforts for this script. It has proven to be a very valuable tool for gathering ISA data into an easily understood form. Use it, live it, love it…
Log analysis;
  ISA logs are your first, best place to go for ISA behavioral information; spend the time to get familiar with them. They contain valuable data for all the traffic that ISA sees. You can even use them along with NetMon to determine what a particular app is trying to do
  Windows Event logs are the second most important data source for ISA troubleshooting. Many of the alerts ISA throws are also found in the event logs with some helpful data appended to them (SMTP filter events, for instance)
Basic Windows and network troubleshooting; name resolution(!), routing, RRAS, VPN, the list goes on. ISA merely provides some configuration wizards and the traffic controls to allow or deny traffic. The functionality and problem resolution techniques you use without ISA are only slightly modified with ISA in place.
  Name resolution – remember the ISA DNS cache-O-death for Web Proxy and Firewall client requests. SecureNAT clients require their own name resolution service
  Routing – ISA has only the most basic of routing functionality; no more than that provided by Windows and/or RRAS

## Slide 24: ISA Logs
IP Logs
  All traffic that is refused by the mspfltex service (can log “allowed” as well)
WEB Logs
  All the traffic that is handled by the w3proxy service
FW Logs
  All the traffic that is handled by the fwsrv service
Log Configuration Option
  W3C format
  ISA format
Notes: ISA Log analysis is best approached in a per-service context. That is, data is written to the logs is based on which service (Web Proxy, Firewall, Packet Filter) actually controlled access through the ISA.
Packet filter Logs – By default, these contain data pertaining to traffic that was dropped by the packet filter (mspfltex) service. It is poossible to configure the PF service to log allowed traffic as well, but that’s really only valuable for troubleshooting, since the WEB and FW logs also contain successful traffic passage through ISA.
WEB logs – These logs contain data on all traffic that was processed by the WEB proxy (w3proxy) service, both outbound and inbound (reverse proxy). You will also find cache hit data in these logs if you enable it.
  ISA help lists the expected data to be found in the various fields
FW logs – These logs contain data on all traffic handled by the firewall (fwsrv) service, both inbound and outbound. Note that all WEB proxy traffic is also passed through the FW service, and as a result, is also logged here.
  Some of the most useful log entries were left out of the help. They can be found here: http://support.microsoft.com/default.aspx?scid=kb;en-us;Q284818

## Slide 25: Packet Filter Logs
All traffic that was refused (ignored) by the Packet Filtering Service (mspfltex)
Can log “allowed” traffic, but makes for huge log files
Notes: You can obtain some very detailed traffic data from this log.
You can also overload yourself with irrelevant data by logging allow filters.

## Slide 26: WEB Proxy logs
All traffic that was either allowed or denied by the Web Proxy Service
Client credentials depend on settings in the Incoming and Outgoing web requests listeners
Also contains cache hit data
Notes: The only data found here is from Web Proxy requests, or invalid requests made to the Web Request Listeners.
ISA Logs everything! Anonymous request logging is required; those requests happened, and must be recorded

## Slide 27: Firewall Service logs
All traffic that was allowed or denied by the Firewall service.
Useful for determining what protocols / ports are being used by an app
Notes: Here’s where the http://support.microsoft.com/default.aspx?scid=kb;en-us;Q284818 article comes in very handy
The FW log is probably one of your handiest tools for evaluating ISA and client actions.
Event the traffic allowed by the Web Proxy service is logged here

## Slide 28: Event Logs
Application Event logs
  All ISA services log here
Security Event Logs
  Depends on your Auditing
System Event Logs
  Can also assist with issue resolution
Notes: Application logs – often contain details not found in the alerts or in the logs. For instance, an SMTP Filter event may include the data that caused the filter to fire
Security logs – these depend on your audit security settings. If you don’t enable auditing and then set it for certain objects / resources, you don’t get the logs
System logs – these will indicate service status events and other system-related relevant information.

## Slide 29
http://www.microsoft.com/ISAServer
http://www.isaserver.org
Notes: <header>
<date/time>
Slide Objective: End of presentation.
Opportunity to take additional questions.