## Slide 1: Taranis: Invisible Traffic Redirection on Ethernet Switches
Jonathan Wilkins
jwilkins@bitland.net
http://www.bitland.net/taranis
Copyright 2001 © Jonathan Wilkins
Notes: Presentation available at the above URL
Feel free to email me questions
Ask questions throughout

## Slide 2: Introduction
We’ll cover:
  Ethernet ARP Cache Corruption (briefly as background)
  Ethernet Switch CAM Table Poisoning
  Defenses
Expected background
  You know what a sniffer is
  You are familiar with network traffic analysis and basic network protocols
Notes: If I’m discussing something you’re already familiar with, please bear with me, I wanted this talk to be useful to a wide audience.. We’ll get to the good stuff quickly..

## Slide 3: OSI Model
Application – DNS, SNMP, HTTP
Presentation – SSL
Session –
Transport – TCP, SPX, NetBIOS
Network – IP, IPX, ARP, Routers
Data Link – Ethernet, Bridges, Switches
Physical – Cabling, Hubs, Repeaters
Notes: TCP/IP squishes the top layers together

## Slide 4: How Ethernet Works
Frame Layouts and ARP

## Slide 5: Ethernet
Data Link layer
Ethernet Header
Destination Address
6 Bytes
Source Address
6 Bytes
Type
2 Bytes
Typical Ethernet Header for IP packet
00:01:03:DC:A5:0C
00:01:03:C4:49:00
0x0800
Byte
12
Byte
13
Byte
14
Byte
8
Byte
9
Byte
10
Byte
11
Byte
5
Byte
4
Byte
6
Byte
7
Byte
1
Byte
2
Byte
3

## Slide 6: Ethernet Address Resolution
For machines to be able to communicate with each other at all, they each need to have a list of IP address to Hardware address mappings
For these machines to be able to communicate in an ad-hoc fashion, they need to have some way to query for IP address to Hardware address mappings.
This is done through ARP (Address Resolution Protocol)

## Slide 7: ARP
Normally, when a host needs to talk to another host, it checks it’s ARP cache to see if it already has an entry for the other host. If it does, just uses it.
If not, it sends out an ARP query.
Gratuitous ARP

## Slide 8: ARP Request Format
Ethernet Frame
ARP Request
Destination Address
Source Address
Type
Hardware
Type
Protocol
Type
Hardware
Size
Protocol
Size
Target HW Address
Target IP Address
Sender HW Address
Sender IP Address
Operation
Byte
12
Byte
13
Byte
14
Byte
8
Byte
9
Byte
10
Byte
11
Byte
5
Byte
4
Byte
6
Byte
7
Byte
1
Byte
2
Byte
3

## Slide 9: Diagram of ARP Request Packet
Ethernet Frame
ARP Request
Destination Address
FF:FF:FF:FF:FF:FF
Source Address
00:01:03:DC:A5:0C
Type
0x0806
Hardware
Type
0x0001
(Ethernet)
Protocol
Type
0x0800
(IP)
Hardware
Size=6
Protocol
Size=4
Sender HW Address
00:01:03:DC:A5:0C
Sender IP Address
10.0.1.71
Target HW Address
00:00:00:00:00:00
Target IP Address
10.0.1.10
Operation
0x0001
(Request)
Byte
12
Byte
13
Byte
14
Byte
8
Byte
9
Byte
10
Byte
11
Byte
5
Byte
4
Byte
6
Byte
7
Byte
1
Byte
2
Byte
3
Notes: Draw red circles around important fields

## Slide 10: Ethereal Display of ARP Request

## Slide 11: ARP Reply Format
Ethernet Frame
ARP Request
Destination Address
Source Address
Type
Hardware
Type
Protocol
Type
Hardware
Size
Protocol
Size
Sender HW Address
Sender IP Address
Target HW Address
Target IP Address
Operation
Byte
12
Byte
13
Byte
14
Byte
8
Byte
9
Byte
10
Byte
11
Byte
5
Byte
4
Byte
6
Byte
7
Byte
1
Byte
2
Byte
3

## Slide 12: Diagram of ARP Reply Packet
Ethernet Frame
ARP Request
Destination Address
00:01:03:DC:A5:0C
Source Address
00:01:03:C4:49:00
Type
0x0806
Hardware
Type
0x0001
(Ethernet)
Protocol
Type
0x0800
(IP)
Hardware
Size=6
Protocol
Size=4
Sender HW Address
00:01:03:C4:49:00
Sender IP Address
10.0.1.10
Target HW Address
00:01:03:DC:A5:0C
Target IP Address
10.0.1.71
Operation
0x0002
(reply)
Byte
12
Byte
13
Byte
14
Byte
8
Byte
9
Byte
10
Byte
11
Byte
5
Byte
4
Byte
6
Byte
7
Byte
1
Byte
2
Byte
3
Notes: Reverse Target and Sender
Request is Broadcast, Reply is Unicast

## Slide 13: Ethereal Display of ARP Reply

## Slide 14: The Role of Switches
Switches increase performance by creating virtual circuits
  Aggregate bandwidth is boosted
Switches don’t add security
A VLAN is functionally a separate switch. Feel free to interchange the words Switch and VLAN

## Slide 15: ARP Cache Corruption
When a given host sends out an ARP request for a host’s IP address, (the network gateway is the usual target) the attacking host replies to it, using it’s own hardware address.
Traffic then goes through the attacking host, thereby giving it access to all kinds of interesting information.
This doesn’t disrupt normal traffic, as the attacking host forwards all traffic to the correct gateway host.
Notes: Dug Song’s ARPSpoof just sends out a gratuitous arp reply every 2 seconds to the broadcast address (ff:ff:ff:ff:ff:ff)

## Slide 16: Detecting ARP Cache Corruption Attacks
Presuming that an administrator has access to a monitoring port on the switch, detection is easy, just check for multiple MAC addresses responding to a given IP address.
ARPWatch can do this through sniffing or by SNMP
  (ftp://ftp.ee.lbl.gov/arpwatch.tar.gz)

## Slide 17: A New Attack - Reasoning
Switches can auto-configure themselves
Switches can either have a single host or another switch/hub on each port
When a device is moved from one port to another, nothing needs to be done to the switch.
Therefore: The switch must automatically maintain a list of Ethernet address to port mappings
Question: Can we trick the switch into sending traffic to the wrong port by tricking it’s auto-configuration logic?
Notes: Axiom: Anything that makes security easier, probably creates a security flaw.

## Slide 18: A New Attack - Reasoning
What attacks are likely?
  Send a packet with the victim’s Ethernet address and see if it will start sending that data to both ports (Limited Hub Mode)
  Send a packet with the victim’s Ethernet address and see if it will redirect traffic
  See if we can resend the traffic and have it picked up by the victim for a full MITM attack
  Send packets with source addresses of other hosts on the network on our port and try and get the switch to drop into hub mode (a la macof )
Notes: Less secure than Hub, DOS possible – log host data redirected

## Slide 19: Results
We weren’t able to get any tested switch to send to multiple ports
We weren’t able to get any tested switch to drop to hub mode
We were able to get traffic redirected to a different port on all tested switches
We weren’t able to get a simple MITM attack functioning, but we have some ideas that may be sufficient to extend the attack
We were able to generate an easy DOS on all tested switches

## Slide 20: Why it works
Switches attempt to over simplify the complicated affair of configuration
Only expensive managed switches allow port locking and even there, the administrative cost of doing so is prohibitive

## Slide 21: What is the CAM Table?
Basically a really efficient lookup table
Present on all modern switches
CAM == Content Addressable Memory
For more information on the CAM table and how it is updated check out http://routergod.com/gilliananderson or http://www.isdmag.com/editorial/1998/systemdesign9801.html

## Slide 22: What is the CAM Table?
This internal table looks something like this:
Port | Ethernet Addresses | Host or Uplink
1 | 01:00:af:34:53:62 | Single host
2 | 01:e4:5f:2a:63:35 00:c1:24:ee:62:66 ... | Switch or Hub
3 | 11:af:5a:69:08:63 00:17:72:e1:72:70 ... | Switch or Hub
4 | 00:14:62:74:23:5a | Single host

## Slide 23: Switch Behavior
3 update behaviors were seen
  Last packet updates CAM table
  Timeout before CAM table update
  Port is locked
Each approach has problems
  Last packet updates – Trivial to redirect traffic
  Timeout – Once port is redirected, keeping control is easy. Requires less traffic to keep control
  Lock – Huge administrative burden associated
Notes: Locked ports extremely rare.. Almost no one knows this is an option

## Slide 24: Results – Switch Update Behavior
Cisco 2900 MXL and Cisco 2900 XL (Port Security Off) | Timeout (~30 seconds)
Cisco 2900 MXL and Cisco 2900 XL (Port Security On) | Traffic redirected only on reboot or cable disconnect
LinkSys EZXS88W | Last Packet Updates
HP ProCurve 2424M | Last Packet Updates
3Com SuperStack II/1100 | Last Packet Updates

## Slide 25: Results – Why it’s Invisible
There’s no way to tell which port traffic is coming from at the Ethernet level
All unmanaged switches are therefore totally vulnerable
There are no tools to track the MAC address to Port mappings for the few managed switches that have a way to query these mappings

## Slide 26: Results - Why It’s Invisible
Even if an administrator attempted to poll the switch continually, this attack could be slipped between queries
Only does protocol specific traffic. Other hosts have no way to tell that there has been a substitution

## Slide 27: ARP Corruption Versus CAM Table Poisoning
Layer 3
ARP provides a good Man In The Middle attack
Tools exist to detect this attack. The attack consists of packets with a definite format
Layer 2
No good Man In The Middle attack
Impossible to generate a single signature for the attack

## Slide 28: Taranis
Proof of concept code
Taranis spawns two threads
  First thread loops, spoofing packets with an Ethernet source address of the target machine – This tricks the switch into redirecting traffic
  Second thread pretends to be a POP or IMAP server
Any connection attempts to port 110 (POP) or 143 (IMAP) are handled by Taranis

## Slide 29: POP3
A normal POP login sequence looks like this:
[jwilkins@toxygene ~]$ nc localhost 110
+OK QPOP (version 2.53) at mail.net starting. <39898.1010976721@mail.net>
USER jwilkins
+OK Password required for jwilkins.
PASS mypasswd
+OK jwilkins has 592 messages (7597672 octets).
QUIT
+OK Pop server at mail.net signing off.

## Slide 30: IMAP
A normal IMAP login sequence looks like this:
[jwilkins@toxygene ~]$ nc localhost 143
* OK mail.net IMAP4rev1 v12.264 server ready
A00001 LOGIN "jwilkins" “mypasswd"
A00001 OK LOGIN completed
A00002 LOGOUT
* BYE mail.net IMAP4rev1 server terminating connection
A00002 OK LOGOUT completed

## Slide 31: Taranis
For POP:
  When a SYN is seen, a SYN/ACK is sent
  When an ACK is seen, the POP banner is sent
  Expects USER <username>\r\n
  Sends “OK”
  Expects PASS <password>\r\n
  Resets the connection

## Slide 32: Taranis
For IMAP (even easier):
  When a SYN is seen, a SYN/ACK is sent
  When an ACK is seen, the IMAP banner is sent
  Expects A0001 LOGIN “user” “password”\r\n
  Resets the connection

## Slide 33: Taranis
Taranis - POP3
Taranis - IMAP
Client | Server
SYN | SYN/ACK
ACK | +OK QPOP (version 2.53) at mail.net starting. <28815.1011055535@mail.net>\r\n
USER foo\r\n | OK\r\n
PASS bar\r\n | RST
Client | Server
SYN | SYN/ACK
ACK | * OK mail.net IMAP4rev1 v12.264 server ready\r\n
A00001 LOGIN “user” “pass”\r\n | RST

## Slide 34: Taranis - Demo
Break for demonstration of Taranis

## Slide 35: Taranis – Future Directions
Proof of concept code
Any other protocol could be spoofed in this way
A replacement log host seems like a fun idea
An attacker could even just reconfigure a complete system with the target server’s IP address and Ethernet MAC address
There doesn’t seem to be a way to perform a perfect man in the middle (MITM) attack with this technique
It is, however, possible to queue packets and perform a protocol independent attack

## Slide 36: Defences
This attack can be almost invisible.
  Ethernet doesn’t indicate what port a given frame came across
A generalized detection heuristic is difficult. Depending on the type of switch, the attack can be successful with just one properly timed packet. Cryptography is the only real defense.

## Slide 37: Defences
Do all clear-text logins via SSH or stunnel
  This isn’t perfect.. Man in the middle attacks are possible since users still don’t have any clue about security and may accept a bad certificate or key
  See Dug Song’s WebMITM and SSHMITM at http://www.monkey.org/~dugsong/dsniff
System must provide strong authentication
  Use SSH public keys or Stunnel with certificates

## Slide 38: SSH Tunnels
ssh -L 110:mail.net:110 -l username -N mail.net
Point your mail client at localhost instead of mail.net
SSH will prompt you for a password
You can use ssh-agent to simplify this
SSH is available for Windows
This does require shell access to the remote host. Obviously, if shell access isn’t required for any other reasons, stunnel would be a better solution

## Slide 39: Stunnel
Full information on stunnel and certificates is available at http://www.stunnel.org/examples/client_cert.html
On the client
  stunnel –c –p mailnet.pem –d pop3 –r mail.net:pop3s
On the server
  stunnel –p /path/to/stunnel.pem –d pop3s –r pop3
Stunnel is available for Windows

## Slide 40: Summary
Ethernet does not provide a private channel. It wasn’t designed for this.
All sorts of protocols that are common on intranets use clear text authentication (POP3, IMAP, SNMP, Telnet, FTP, Log servers, CVS)
If an attacker gets intranet access, you’ve probably lost unless you have strong authentication and good crypto.
Now that we’re all aware of the need for protecting authentication details, setting up encrypted tunnels is a necessity
Notes: Determine the best close for your audience and your presentation. Close with a summary; offer options; recommend a strategy; suggest a plan; set a goal. Keep your focus throughout your presentation, and you will more likely achieve your purpose.

## Slide 41: Summary
Taranis allows
  Invisible traffic redirection
    No general heuristic possible for this attack
    Polling the CAM table may work sometimes
  Invisible Denial Of Service
    Rendering switches less secure than hubs in certain situations
  Cryptography is the best protection
  Intranets shouldn’t be trusted
Notes: All unmanaged switches need to be replaced
The operating systems of all managed switches need to be updated to add port-change information
Port lock mode extremely expensive to maintain

## Slide 42: References
Taranis
  http://www.bitland.net/taranis
  http://www.bitland.net/taranis/taranis.[pdf,ppt]
Setting up encrypted tunnels
  SSH (http://www.openssh.com)
    http://www.employees.org/~satch/ssh/faq/
  Stunnel (http://www.stunnel.org)
    http://www.freebsddiary.org/stunnel.php
Ethereal (http://ethereal.zing.org)

## Slide 43: Thanks
Jesse jesse@bitland.net for the original idea
Skyper skyper@segfault.net for all the help testing switches
Ed ed@apache.org help testing switches